## Slide 1: Creating the transport model
NOTE FOR ANYONE LOOKING AT THIS FILE:
This is just an old presentation I did, it contains some old notes that are probably out of date. I have kept it here in case it contains any breadcrumbs which may help someone who is interested.

## Slide 2: To do list
Implementation of wfh in transport model vs buildings model.
Create easy visualistations file for communicating with people outside the model (e.g. EGEEC efficiency meetings, outlook scenario planning, presentations, etc.)
Double check sales dists with 8th
Replicate an economy, maybe Thailand.
  Then I will have an idea of how long it would take to configure a run and also how accurate the model is to what we expect
    Time estiamtes
    Accruacy
What others will need from my output:
  Electricity for power model
Contact adb
Work out how well iTEM works
Non road vehicles and agricultural model
Is the identity of the model still a ‘knowledge based’ model?
Create a way to scale the data according to what may be happening in other models, e.g. increasing ev use, will increase mining, increasing agriculture may increase non road use?
How to show effect of an economy focusing more on trains. Perhaps need some shifting of activity between the non-road and road model?
  Could just incorporate it into the vehicle sales share model, and set travel km per stock to 1 for all non road?
Incorp 2w into freight data somewhow
Do we need a sort of S curve for activity growth based on stocks/population?

## Slide 3: Intention
Focus on the most important outputs from the model. How can I provide forecasts of those? (stocks and energy use)
Make it relatively easy to use/understand.
Make a model that can be used as a model not a single use forecaster.
Produce good documentation/methodology documents so that I can communicate my model with others (in and out of APERC)

## Slide 4: Documentation
Simple coding style (scripts, line by line)
https://github.com/asia-pacific-energy-research-centre/transport_model_9th_edition/wiki
  Publicly accessible
Documentation documents
  Excel simulation of model
  Word document

## Slide 5: Thinking in terms of systems
Develop systems to replace manual processes with a goal of saving time in the long run
  E.g. base year variable
Create systems that are simple but cover possible future needs.
Create systems with the intention that you will reuse them
Create systems that abstract the tasks you need to think about, so you can think about the research instead.
Notes: For example for data categories, define a set of categories like vehicle type, drive type, fuel types, etc, but keep the possible categories within them and operations on them as open as possible. For example, avoid keeping data limited to a prespecified set of fuel types so it’s easy to introduce new fuel types later.

## Slide 6: Things it would help me for us to focus on
Choosing a base year
  It seems that if we don’t choose 2019 as base year, we should choose 2023, but this will be difficult to guarantee data for.
  Important because it is important to know what years I need data for when I ask people for it

## Slide 7: Next few slides: Columns, variables and inputs
Category/column name | Description | Format
Year |  | 
Economy | labelled with APERC naming convention, eg, 01_AUS = Australia. There is a mapping from these codes to their real names in the config/utilities folder. | The same format as the economy labels
Transport Type | either 'Passenger' or 'Freight'. | All in lower case
Medium | either of ['road', 'air', 'ship', 'rail'] | All in lower case
Vehicle Type | if the medium is not road, this is the medium, but if the medium is road, it can be one of ['2w', 'ht', 'lt', 'lv'] | All in lower case
Drive | if the medium is not road, this is the medium, but if the medium is road, it can be one of ['d', 'g', 'bev', 'cng', 'phevg', 'phevd'] | All in lower case
Scenario | One of the scenarios used in the model. | Begins with Capital letter
Fuel | Any fuel type used in the transport system. Fuel type named using the APERC naming conventions. The mappings for these to other naming conventions used in APERC should be in ./config/utilities/ | All in lower case
Measure | A label to describe what measure the data is in. | All in lower case
There are ?4000? Rows per economy in the first year. So it can be difficult to guarantee data quality. For this reason I have tried to cut as many unnecessary variables as possible, while keeping what I thought was expected from the model, i.e. a stocks output.

## Slide 8
The output is the same as the base year data, forecasted to the maximum year.
Base year data:
Energy
Freight tonne km
Passsenger km
Energy use by drive type (road only)
Energy use by fuel type
Activity
Turnover rates (road only)
Occupancy and load factors (road only)
New vehicle efficiency (road only)
Stocks (road only)
Other factors
Fuel mixing (e.g. biofuel mix %)
Hybrid electricity usage % (road only)

## Slide 9
Growth rates and user defined inputs
Turnover growth rates
Occupancy and load factors growth
New vehicle efficiency growth
Non road efficiency growth
Vehicle sales share
Demand/supply side fuel mixing
Activity growth rate
These can all be defined by the user before running the model.
Some are unlikely to be changed, such as turnover and occupancy, but some have a lot of effect on the output from the model, such as vehicle sales share and efficiency growth.
They can also just be set to 1 or 0 so that they have no effect. This reduces complexity at no cost.

## Slide 10: Vehicle sales distribution
The way new stocks are allocated each year is:
  Distribution of sales for each vehicle/drive type within passenger or freight transport that adds up to 1
  Each year there is a set amount of activity that needs to be satisfied by transport in each transport type. The stock sales distribution determines what vehicles and drives the activity is satisfied by.
    Using the expected activity per vehicle stock (varies with occupany_load_rate), calculate the amount of new stocks needed to calculate that new activity.
    New activity needed each year is the sum of turnover, surplus stocks and activity growth from macro growth.
Chose this way because it is:
  Semi-realistic view of real world
  Easy to think about when working with the input data (vehicle sales distribution)
  Can identify what distribution of sales are actually needed to reach goals.

## Slide 11: What happens if there is negative growth?
Surplus stocks are used to model this. It is unlikely they will ever be used but it seems important to consider.
Unfortunately it makes things a bit more complicated in the model. One day I will go back over this and consider whether its important enough to keep in version 2.

## Slide 12: Output analysis
Can create further data using things like battery price forecast and, emissions factors.
Can look at the amount of EV’s required to meet goals like 100% EVs in California by 2035. Can then adjust growth rates or user adjustments in input data to make scenarios where this happens.
Have scripts written to create standardized graphs from outputs. As I create more and more graphs, this will get easier because I wont need to write the code again.

## Slide 13: Some issues I am still unhappy about
Fuel mixing for demand vs supply side. Not natural to understand.
  To represent the way that biofuels are mixed there is supply side mixing for any fuel that is used in the demand side.
  E.g. for a diesel internal combustion car, the demand side mix will put all use into diesel. However, the supply side mix is applied afterwards and may split all the diesel use into 0.05 biodiesel and 0.95 for diesel.
Most of my time is/was spent on data cleaning ):
Notes: E.g. There are a lot of variables to consider when trying to forecast the share of new vehicles in each drive type for a each vehicle type for each year for each economy. Sometimes it is possible to determine exactly what share of Light vehicle we expect to be EV’s by 2030, but sometimes we just want there to be ‘a bit more than what we have forecasted already’… I’ve made it so you can ‘add 1’ using the user adjustments, but I think it would be better to create tools that require the user to state exactly how much of each thing they want.

## Slide 14: Working with other transport modellors around the world
To do

## Slide 15: Computer generation of input data
To make things easy I plan to create a lot of input data using code, rather than manual adjustments. Becvausae of the number of inputs this will be reallyu useful.

## Slide 16: Visualising data
It’s important that it is easy to inspect the outputs from the system.
  Useful for my own analysis
  Useful for communicating with the economy’s
Big effort is being put towards developing easy-to-use plotting of charts I expect I will use often.

## Slide 17: Data cleaning
Often there is no easy way about this, however I think I have learnt some handy tricks:
  Github copilot for code
    Speeds up replicated processes
    For new processes you cannot remember in code
  Keeping copies of the cleaning that you do is important for understanding the quality of your data and in case you need to redo something. This is more difficult when working with spreadsheets only
  keeping your goal in mind so that you know when a cleaning process may be too tune consuming and a shortcut should be taken (e.g. working out how accurate your data needs to be)

## Slide 18: Keeping track of changes made and information
We need to be able to state what assumptions we have made so keeping an archive of all input data for each scenario is important. By keeping all input data in one dataframe or spreadsheet, this will be more easy.
  Also using the date and time that the model was run as an ID for the input and output data is a good trick.
  Once you build this kind of system it’s easy to replicate.

## Slide 19: The importance of clear documentation
What I like to do:
  Take shortcuts at the sacrifice of tidiness
  Don’t be scared of keeping something vague if there is a clear way the reader can learn about it by using the system.
    Can easily get bogged down in defining how variables are calculated, but if the code is clear, the user can just find the calculation in the code. Plus this encourages them to read the code, which can be the hardest step.
    Things like reasons for naming a folder ‘workflow’ should be self explanatory and if they aren’t then the folder isnt named correctly
  Rely on formatting, styles, tables and flow charts.
  Try to avoid explaining ‘why’ if this can be explained by showing ‘how’.
    There are many ways of clacualting something, but if something is done correctly then showing how it is done often will explain itself.